## Slide 1
TELECOM DIGITAL TWIN · AS-BUILT REVIEW
CER-Intent Digital Twin
Architecture, what works today, and the roadmap for TeraFlowSDN, ns-3 and Ceragon microwave hardware
IMPLEMENTED
works end to end in code
PARTIAL
real code, with limits
MOCK
hard-coded or simulated output
PLANNED
design or docs only
Based on cer-intent @f2c3fea · tfs-ns3-digital-twin @a9ccad6 · teraflowsdn @1e91cf2 · September 2026
CER-Intent
intent → config
TeraFlowSDN
SDN controller
ns-3.45
discrete-event twin
Ceragon MH-T261
60 GHz radio
Notes: This deck documents the system as it is built, not as it was first pitched. Each capability carries one of four statuses: IMPLEMENTED (works end to end in code), PARTIAL (real code with known limits), MOCK (the UI or API returns hard-coded or simulated values), PLANNED (only in docs or slides). Sources: code review of efidvir/cer-intent (commit f2c3fea), efidvir/tfs-ns3-digital-twin (a9ccad6) and efidvir/teraflowsdn (1e91cf2), plus the CER-Intent audit log data/audit_log.jsonl. Numbers on the operating-data slide are produced by docs/deck/audit_stats.py.

## Slide 2
MOTIVATION
Why this project exists
Purpose: let operators state what they want in plain words, test it in a digital twin, and only then change the live microwave network, automatically and safely.
WHY
Weather moves capacity
Rain fade at 60–80 GHz can cut a link from 1 Gbps to 100 Mbps.
Changes are manual and risky
CLI work per radio; a bad change hits live traffic.
Tools don't talk
Intent, SDN, simulator and radio use different languages and clocks.
AI needs a safe sandbox
Agents must be tested before they touch the network.
GOALS · STATUS TODAY
G1
Intent → configuration through the SDN controller
PARTIAL
G2
Every change tested in the ns-3 twin before commit
PARTIAL
G3
Closed loop on real radios: verify, then roll back
PLANNED
G4
Standard interfaces end to end, no vendor lock-in
PARTIAL
G5
AI/ML agents trained and gated in the twin
PLANNED
Notes: Purpose: an intent-driven, twin-validated closed loop for microwave and millimetre-wave transport in 5G/6G networks, built on the open-source ETSI TeraFlowSDN controller, the ns-3 simulator and Ceragon MH-T261 radios. Why: (1) at 60-80 GHz, rain attenuation drives adaptive modulation down; the ns-3 scenario models hop-1 rate falling from 1 Gbps to 100 Mbps under heavy rain. (2) Radio changes are done per device and a mistake lands on live traffic. (3) Intent, SDN, simulator and radio speak different protocols on timescales from microseconds to days. (4) AI agents, such as reinforcement-learning policies, need an isolated place to train and be validated. Goals and where they stand: G1 intents reach TFS and the radio driver (PARTIAL: key mismatch, canned read-back). G2 the ns-3 scenario runs over SSH but its results do not gate commits yet (PARTIAL). G3 verify and rollback after commit are not implemented (PLANNED). G4 RESTCONF/YANG is real; TMF921, TS 28.561 and CAPIF are labels (PARTIAL). G5 no ML in the loop yet (PLANNED). The gap register and roadmap later in the deck show how each goal gets closed.

## Slide 3
THE PROBLEM
Four components, four languages, four clocks
1 µs
1 ms
1 s
1 min
1 h
1 day
Operating timescale (log)
Intent (CER-Intent)
natural language / JSON
minutes – days
SDN (TeraFlowSDN)
REST NBI · gRPC services
seconds
Simulator (ns-3.45)
C++ event queue
microseconds
Radio (MH-T261)
RESTCONF · PHY
sub-ms
Adapters translate both the protocol and the clock between neighbours.
Notes: Unchanged from the earlier deck: the four parts run on timescales from microseconds (ns-3 events) to days (operator intent). The adapters described next translate protocol and time between them.

## Slide 4
AS-BUILT ARCHITECTURE
What is actually wired together today
CER-Intent
Flask + Socket.IO :5000
parser · architect · reconciler
IMPLEMENTED
TeraFlowSDN
microk8s · NBI :8080
clients use localhost:8088
IMPLEMENTED
Ceragon MH-T261
192.168.1.225 · RESTCONF
device ctu-96
IMPLEMENTED
ns-3.45 on cersrv-029
tsn_wifi_ceragon scenario
SSH + JSON markers
PARTIAL
Twin API + bridge
:9100 what-if = formulas
:9099 bridge output unused
MOCK
PUT device
driver 22
direct GET of candidate datastore (health probe only)
SSH run
poll 1 s
Only the solid arrows move real configuration. The twin API and bridge are not yet in the loop.
Notes: CER-Intent (cer-intent/run.py, cer_intent/api/server.py) serves REST and Socket.IO on :5000 and writes to TeraFlowSDN with PUT /tfs-api/device/{uuid} carrying CONFIGACTION_SET rules (cer_intent/device/adapter.py TeraFlowAdapter, device/tfs_client.py). Clients default to TERAFLOW_URL=http://localhost:8088; the TFS NBI service listens on 8080 (teraflowsdn/manifests/nbiservice.yaml), so 8088 is a local port-forward or proxy. TeraFlowSDN is deployed with microk8s via my_deploy.sh with only context, device, pathcomp, service, nbi and webui. The Ceragon driver (DEVICEDRIVER_CERAGON = 22) pushes RESTCONF to the MH-T261 at 192.168.1.225 (manifests/ceragon_mh_t261_descriptor.json). ns-3.45 runs on cersrv-029: tsn_simulation_runner.py SSHes to efid@cersrv-029 and parses JSON between ===TSN_METRICS_START/END===. If SSH fails, it returns constants that are still labelled as ns-3 output, hence PARTIAL. tfs_digital_twin_api.py (:9100) computes what-if results with closed-form formulas; ns3_tfs_runtime_bridge.py (:9099) polls TFS every second and writes ns3_link_state.json, which no ns-3 program reads. Hence MOCK. The red dashed path: the dashboard's 'physical write' is a GET of https://192.168.1.225:80/restconf/ds/ietf-datastores:candidate used as a health probe (web_dashboard.py, cer_intent/api/digital_twin_routes.py).

## Slide 5
CODE MAP
Three repositories, one system
cer-intent
45 Python files · 9.1k lines (core)
Intent parser, schema, validator
Rule-based architect with 9 skills
TFS + RESTCONF + XML adapters
Reconciler, audit log, dashboards
Vendors a copy of the twin repo in tfs_unity/
tfs-ns3-digital-twin
26 Python files · 8.7k lines · 22/22 tests
TFS → ns-3 C++ generator
ns-3.45 TSN / 60 GHz scenario
Twin API :9100, bridge :9099
Fidelity governor, web dashboard
Modules duplicated at root and in src/
teraflowsdn
upstream TFS + Ceragon driver (881 lines)
CeragonDriver, driver enum 22
RESTCONF client: stage → commit
51 YANG models (radio-bridge-tg)
MH-T261 and IP-50C descriptors
Upstream history squashed; version label unverified
Notes: cer-intent: core package cer_intent/ (parser, schema, validator, yang_builder, translators, architect, device adapters, assurance, api). tfs_unity/ is a copy of the tfs-ns3-digital-twin repo; ceragon_tfs_adapter/ is an installable package; tfs_upstream_contribution/ holds the proposed TFS driver patch. tfs-ns3-digital-twin: Python modules exist at the repo root and again in src/. Five are identical; tsn_simulation_runner.py has diverged (404 lines at root, 236 in src/). Tests: 22 pass (python -m pytest tests). teraflowsdn: one squashed commit. Custom code is src/device/service/drivers/ceragon/ (CeragonDriver.py, client.py, templates.py, models.py, Tools.py, 51 YANG files), proto enum DEVICEDRIVER_CERAGON = 22, device type ceragon-wireless, and two descriptors in manifests/. The README calls this TFS 7.0; the code does not confirm a version.

## Slide 6
INTENT LAYER · CER-INTENT
From a sentence to device configuration
1 Parse
Gemini 1.5 Flash, regex fallback
IMPLEMENTED
2 Validate
topology + capability matrix
IMPLEMENTED
3 Plan
9 rule-based skills
PARTIAL
4 Approve
human gate (HTTP 202)
IMPLEMENTED
5 Apply
TFS · RESTCONF · simulated
IMPLEMENTED
Chart: Architect strategies chosen (audit log)
| MRMC Script Upgrade | 1+1 HSB Protection | ACM Floor Hardening Rain | TX Power Adjustment | Network Already Efficient
Plans | 22 | 9 | 6 | 4 | 1
Real operator inputs
“Increase capacity on link-A-B to 5 Gbps for eMBB slice”
“Set ACM range 64QAM to 2048QAM on sector-south links”
“Create slice slice-uran-6g with 1 Gbps on Ceragon MH-T261”
Notes: 1 Parse (cer_intent/intent_parser.py): Google Gemini (GEMINI_MODEL, default gemini-1.5-flash) with a schema prompt and three few-shot examples; without a key it falls back to regex/keyword rules; JSON input skips parsing. Eight intent types: capacity, qos, modulation, resilience, slice, energy, sync, security (intent_schema.py, Pydantic). 2 Validate (intent_validator.py): topology and the DEVICE_CAPABILITIES hardware matrix. 3 Plan (architect/agent.py): nine rule-based skills score strategies by a heuristic confidence; the conflict resolver is a mock with time.sleep(0.1). PARTIAL because the 'AI architect' is rules, not a model. 4 Approve: POST /api/v1/intent returns 202 awaiting_approval unless always_apply; POST /intents/<id>/approve resumes. 5 Apply: ArchitectExecutor or legacy translators, then adapter.apply_all (TeraFlowAdapter, DirectRESTAdapter, SimulatedAdapter, IP-50C XML). Chart: counts of 'Architect plan created: <strategy>' events in data/audit_log.jsonl (audit_stats.py). Quotes are verbatim inputs from the same log. Roadmap: add pluggable parsers (on-prem Qwen, Claude) next to Gemini, and grow the skill bank to cover more transport knowledge.

## Slide 7
OPERATING DATA
What the audit log shows
52
intents parsed
1,143
configuration applies
96.7%
accepted by TeraFlowSDN
61
devices configured
Chart: Configuration applies by backend
| TeraFlow | Simulated | IP50CXML
Succeeded | 1026 | 80 | 2
Failed | 35 | 0 | 0
Chart: Intents parsed per month
| 2026-04 | 2026-06 | 2026-07 | 2026-09
Intents | 40 | 1 | 6 | 5
Parse → last apply: median 396 ms (n = 22, 13 under 1 s). 2026-04-13 – 2026-09-23.
Notes: All numbers come from cer-intent/data/audit_log.jsonl (1,444 events, 2026-04-13 – 2026-09-23) via docs/deck/audit_stats.py. TeraFlowAdapter: 1026 succeeded, 35 failed. Failures: 'Cannot reach TeraFlow SDN at http://localhost:8088' (32) and HTTP 500 from the NBI (3). 'Succeeded' means the TFS NBI accepted the config rule; it does not prove the radio changed, because the Ceragon driver's read-back is canned (see the hardware slide). SimulatedAdapter 80 and IP-50C XML 2 applies are local simulations or files. Parse-to-last-apply is measured only for the 22 intents whose applies carry the intent id; the median is 396 ms and the maximum 1076 s, because the long spans include waiting for human approval. One drift event was recorded: 'SNR 11.9 dB on link-A-F may not sustain min modulation 64QAM' (the reconciler works on synthetic telemetry).

## Slide 8
TERAFLOWSDN INTEGRATION
Deployed components and the calls we use
DEPLOYED (my_deploy.sh)
context
gRPC 1010
device
gRPC 2020
service
gRPC 3030
pathcomp
gRPC 10020
nbi
HTTP 8080
webui
HTTP 8004
NOT DEPLOYED (telemetry · analytics · ML)
monitoring
gRPC 7070
kpi_manager
gRPC 30010
telemetry
gRPC 30050
analytics
gRPC 30080
automation
gRPC 30200
forecaster
gRPC 10040
The 10010–10040 ports shown in the old dashboard are mock values.
NBI calls used by CER-Intent and the twin
GET
/tfs-api/contexts
GET
/tfs-api/context/admin/topology_details/admin
GET
/tfs-api/devices · /links
PUT
/tfs-api/device/{uuid} (config rules)
POST
/tfs-api/context/admin/slices
Ceragon device in TFS
DEVICEDRIVER_CERAGON = 22 · type microwave-radio-system · ceragon-mh-t261-ctu-96 @ 192.168.1.225:80
IMPLEMENTED
No TFS Service or PathComp (CSPF) request is made yet.
Notes: Deployed components: teraflowsdn/my_deploy.sh exports TFS_COMPONENTS='context device pathcomp service nbi webui'. Ports from manifests/*service.yaml: context 1010, device 2020, service 3030, pathcomp 10020, nbi 8080, webui 8004. Not deployed but available in the tree: monitoring 7070, kpi_manager 30010, kpi_value_api/writer 30020/30030, telemetry 30050/30060, analytics 30080/30090, automation 30200, forecaster 10040, plus Kafka. These are the natural hosts for streamed KPIs and Python analytics. The old dashboard's gRPC ports 10010/10020/10030/10040 come from mock JSON in web_dashboard.py get_tfs_microservice_state() and cer_intent/api/digital_twin_routes.py. NBI calls: cer_intent/device/tfs_client.py and tfs_api_client.py. Writes are PUT /tfs-api/device/{uuid} with CONFIGACTION_SET custom rules; slices go to POST /tfs-api/context/admin/slices. The dashboard's POST /tfs-api/device/{uuid}/config is not a TFS endpoint. Ceragon: proto/context.proto DEVICEDRIVER_CERAGON = 22; src/device/service/drivers/__init__.py registers it (needs LOAD_ALL_DEVICE_DRIVERS); descriptor manifests/ceragon_mh_t261_descriptor.json. The WebUI device form has no Ceragon checkbox, so devices are added by descriptor.

## Slide 9
SIMULATION ADAPTER · NS-3.45
The TSN-over-microwave scenario the twin runs
STA ×2
802.11n
HtMcs7
Wi-Fi AP ×2
10 Gbps
C0
60 GHz
1 Gbps · 0.15 ms
C1
10 Gbps
0.02 ms
C2
80 GHz
10 Gbps · 0.10 ms
C3 → sink
rain attenuation acts on this hop
TSN flow
128 B every 1 ms · ToS 0xC0 (AC_VO, band 0)
Best effort
1400 B at 150 Mbps × surge factor
Queue
PfifoFast (QoS on) or FIFO · 150 packets
SLA check
TSN mean delay > 1.5 ms or loss > 0.001 %
IMPLEMENTED
fallback when SSH fails:
MOCK
Chart: Hop-1 rate vs rain attenuation (Mbps, scenario rule)
| 0 dB | < 8 dB | 8–15 dB | 15–25 dB | ≥ 25 dB
Rate | 1000 | 750 | 500 | 250 | 100
Notes: Scenario: tfs-ns3-digital-twin/simulation/tsn_wifi_ceragon.cc (ns-3.45). Two stations to two 802.11n APs (HtMcs7), then C0 -60 GHz 1 Gbps 0.15 ms- C1 -10 Gbps 0.02 ms- C2 -80 GHz 10 Gbps 0.10 ms- C3 to the sink. Traffic: TSN flow 128 B at 1.024 Mbps (one packet per ms) with ToS 0xC0, mapped to PfifoFast band 0 and Wi-Fi AC_VO. There is no 802.1Q VLAN/PCP tagging in the simulation; the 'PCP 6' label in the old deck comes from dashboard mock JSON. Best effort: 1400 B at 150 Mbps times the surge factor. Rain: rainLossDb steps hop-1 rate to 750/500/250/100 Mbps at the 8/15/25 dB thresholds; this is a rule, not an ACM model. FlowMonitor results are printed as JSON between ===TSN_METRICS_START/END=== and parsed by tsn_simulation_runner.py over SSH (efid@cersrv-029, 25 s timeout). The Wi-Fi contention, retry and airtime numbers in that JSON are hard-coded. Fallback: if SSH fails the runner returns constants (0.93 ms TSN with QoS, 6.83 / 8.12 ms without) and still labels them as ns-3 output. MOCK. Second path: tfs_topology_to_ns3.py generates a C++ program from the TFS topology (one point-to-point link per TFS link, /30 subnets, optional 500 Mbps OnOff traffic, NetAnim). It produces no metrics yet. The simulation resolution governor (simulation_resolution_governor.py) picks a tier and scales node counts; its per-tier latencies (75, 350, 650, 1150, 35 ms) are constants, not measurements.

## Slide 10
HARDWARE PATH · CERAGON DRIVER
Stage, commit, discard: real RESTCONF, with gaps
TFS device service
CeragonDriver (22)
MH-T261
192.168.1.225
① PATCH candidate datastore
radio · VLAN sub-interface · ACM floor
② if staging fails: discard-changes
POST ietf-netconf:discard-changes
③ POST ietf-netconf:commit
candidate → running
④ read state
returns canned values today
IMPLEMENTED
steps ①–③
MOCK
step ④
Not yet in place
No rollback after commit
discard only runs when staging fails
PLANNED
No telemetry subscription
SubscribeState returns True, streams nothing
PLANNED
Intent keys ≠ driver keys
min/max modulation never reaches the radio
PARTIAL
Dashboard wire log and diff
static JSON, never sent
MOCK
Notes: teraflowsdn/src/device/service/drivers/ceragon/client.py: stage_candidate() PATCHes /restconf/ds/ietf-datastores:candidate; on failure apply_* calls discard_candidate() (POST /restconf/operations/ietf-netconf:discard-changes); otherwise commit_candidate() POSTs /restconf/operations/ietf-netconf:commit. Payloads come from templates.py: radio-bridge-tg:radio, ietf-interfaces sub-interfaces for VLAN slices, radio-bridge-tg-acm:acm-configuration for the ACM floor. CeragonDriver.SetConfig routes by resource key (/radio, /frequency, /operating_parameters, /slice, /vlan, /modulation, /acm, /rain). Gaps: there is no verification after commit and no rollback of a committed change. get_device_state() (lines 95-195) returns hard-coded values (60.48 GHz, SNR 28.5, RSSI -42) and discards the live ietf-interfaces GET. SubscribeState/UnsubscribeState/DeleteConfig return True without doing anything. Key mismatch: CER-Intent sends /interface[name=...]/modulation with min/max modulation, while the driver's modulation branch reads mrmc_script_id, tx_frequency and tx_power_dbm. Most intents therefore change nothing on the radio. The old deck's 'two-phase commit with automatic rollback', the four pre-flight gates and the RESTCONF wire log came from static JSON in web_dashboard.py and cer_intent/api/digital_twin_routes.py (which also label the device 'siklu-radio').

## Slide 11
CLOSED LOOP
Today it detects; the target loop also acts
TODAY
Intent
parse, plan, approve
IMPLEMENTED
Apply
PUT to TFS, driver commit
IMPLEMENTED
Telemetry
synthetic, every 5 s
MOCK
Drift check
thresholds, every 10 s
PARTIAL
Alert
DRIFT state + event
IMPLEMENTED
Remediate
never runs
PLANNED
TARGET
Intent
plus live telemetry
PARTIAL
What-if
ns-3 job per candidate
PARTIAL
Gate
from simulated KPIs
PLANNED
Commit
stage → commit
IMPLEMENTED
Verify
YANG-Push read-back
PLANNED
Rollback
if KPIs regress
PLANNED
Notes: Today: cer_intent/assurance/telemetry_simulator.py generates sinusoidal load and SNR every 5 s; assurance/reconciler.py checks every 10 s (capacity below 80% of target with utilisation above 90%, latency more than 5 ms over target, SNR below 12 dB) and sets DRIFT plus a Socket.IO intent_drift event. It never re-applies; REMEDIATED is never set. The architect receives empty telemetry because app.telemetry_snapshot is never set. Target: every candidate change becomes an ns-3 what-if job, the pre-flight gates are computed from its KPIs instead of constant PASS strings, the driver commits, live telemetry verifies the result, and a committed change is rolled back if KPIs regress. The old '~1.9–2.2 s end-to-end' figure is not backed by any log; measure the real loop time once it exists.

## Slide 12
STANDARDS
Claimed vs implemented
STANDARD
WHAT THE CODE DOES
STATUS
IETF RFC 8040 RESTCONF
Ceragon driver: PATCH candidate, commit, discard
IMPLEMENTED
IETF RFC 7950 YANG 1.1
51 bundled models; payload templates
IMPLEMENTED
IETF RFC 8345 topology
TFS NBI plugin exists; not used by our code
PLANNED
IETF RFC 6241 NETCONF
XML generated by yang_builder, never sent
PARTIAL
TM Forum TMF921 intent
custom schema; :9100 endpoint stores and acknowledges
MOCK
3GPP TS 28.561 NDT
NDTI state enum only; no NDTJob or report
PARTIAL
3GPP TS 29.222 CAPIF
static discovery JSON
MOCK
ITU-T Y.3090 / Y.3092
labels on endpoints and slides
PLANNED
YANG-Push / gNMI
claimed in docs; driver subscribes to nothing
PLANNED
ITU-R P.838 rain
approximate coefficients in formulas
PARTIAL
Notes: RFC 8040: teraflowsdn/src/device/service/drivers/ceragon/client.py and cer-intent/ceragon_tfs_adapter. RFC 7950: 51 YANG files in drivers/ceragon/schemas/yang (radio-bridge-tg-*, IEEE 802.1Q, IETF, Clixon). RFC 8345: TFS has an ietf_network NBI plugin (src/nbi/service/ietf_network) but CER-Intent reads TFS's own topology_details JSON instead. RFC 6241: cer_intent/yang_builder.py builds NETCONF XML; ncclient is a dependency but never used to send it. TMF921: CER-Intent's intent model is a custom Pydantic schema; tfs_digital_twin_api.py POST /api/v1/tmf/tmf921/intent stores the payload and returns 'acknowledged' with no TMF resource model or lifecycle. TMF639 is a minimal GET projection. TS 28.561: only the NDTI states (NULL, INITIALIZING, SYNCHRONIZED, UPDATING, EXECUTING_EXPERIMENT, TERMINATED) in tfs_digital_twin_api.py; the NdtJob model exists only in generate_deck.py. CAPIF: a static JSON descriptor without OAuth or mTLS. Y.3090 is a label on /dti/sync; Y.3092 and Q.5040 appear only in slides and a commit message. YANG-Push and gNMI are claimed in docs only. P.838: approximate k and alpha at 60 GHz in formulas.

## Slide 13
STANDARDS BY INTERFACE
Four interfaces, and the standards that fit each
CER-Intent
LLM + rule agents
TeraFlowSDN
SDN controller
Digital twin
ns-3.45
MH-T261
Ceragon radio
① TMF921 · TS 28.312 · IETF L3NM / slice NBI
② TS 28.561 NDTJob · Y.3092 NDT-m · CAPIF
③ RFC 8345 · RFC 8561 · YANG-Push / gNMI · Y.3092 NDT-p
④ RESTCONF 8040/8527 · YANG · RFC 8561 · TLS
In use today
① TFS native REST NBI
② SSH + JSON, custom REST :9100
③ TFS REST polling every 1 s
④ RESTCONF candidate → commit
Notes: ① CER-Intent agents to TFS (northbound): today TFS native REST (PUT /tfs-api/device, POST slices). Adopt TM Forum TMF921 or 3GPP TS 28.312 for the intent itself, and hand TFS standard service requests through its existing IETF L3NM (RFC 9182), L2NM (RFC 9291) and network-slice (RFC 9543 framework) NBI plugins. ② CER-Intent to the digital twin: today SSH to cersrv-029 plus a custom REST API on :9100. Adopt 3GPP TS 28.561 NDTJob/NDTReport over TS 28.532 operations, which ITU-T Y.3092 calls NDT-m, and expose it through CAPIF (TS 29.222). ③ TFS and the twin: today REST polling every second. Adopt RFC 8345 topology (TFS ietf_network NBI) and RFC 8561 microwave link data for the ns-3 model, and YANG-Push (RFC 8641) or gNMI streaming into TFS KPI/Kafka (Y.3092 NDT-p). Model physics from ITU-R P.838, P.676 and P.530. ④ TFS to the radio: today RESTCONF (RFC 8040) on the NMDA candidate datastore (RFC 8527 path /restconf/ds/ietf-datastores:candidate) with NETCONF commit/discard operations and vendor radio-bridge-tg YANG. Adopt RFC 8561 / ONF TR-532 models, YANG-Push telemetry, TLS 1.3 and NACM. Full list with statuses: docs/STANDARDS_BY_INTERFACE.md.

## Slide 14
STANDARDS BY INTERFACE
What we use, what TFS offers, what to adopt
① Agents → TFS
IN USE
TFS REST NBI
ADOPT
TMF921 intent API
ADOPT
3GPP TS 28.312 intent
IN TFS
IETF L3NM · L2NM
IN TFS
IETF network slice NBI
IN TFS
CAMARA QoD
DE FACTO
MCP tools for agents
② Agents → twin
IN USE
SSH + JSON · OpenAPI
ADOPT
TS 28.561 NDTJob
ADOPT
Y.3092 NDT-m
ADOPT
CAPIF TS 29.222
ADOPT
TS 28.105 · Y.3181
DE FACTO
Gymnasium · ns3-ai
EMERGING
Rel-20 NDT · Q.SDTN
③ TFS ↔ twin
IN USE
TFS REST polling
IN TFS
RFC 8345 topology
ADOPT
RFC 8561 microwave YANG
ADOPT
YANG-Push · gNMI
IN TFS
KPI · telemetry · Kafka
ADOPT
ITU-R P.838 · P.676 · P.530
ADOPT
Y.3092 NDT-p · Y.3093
④ TFS → radio
IN USE
RESTCONF RFC 8040
IN USE
NMDA RFC 8527 · 8342
IN USE
YANG 1.1 · 802.1Q
ADOPT
RFC 8561 · ONF TR-532
ADOPT
YANG-Push telemetry
ADOPT
TLS 1.3 · NACM
DE FACTO
vendor radio-bridge-tg
Notes: Tags: IN USE = our code uses it today; IN TFS = TeraFlowSDN ships it but we do not use it yet; ADOPT = recommended for this interface; EMERGING = still being standardised; DE FACTO = open-source or vendor convention. Notes: TS 28.312 is 3GPP's intent-driven management service; RFC 8527 defines the /restconf/ds/<datastore> paths our driver uses; calling NETCONF commit/discard through RESTCONF operations is a vendor mapping, not part of RFC 8040. MCP (Model Context Protocol) is a de facto way to expose TFS and twin operations as tools for LLM agents. Details and rationale for every entry: docs/STANDARDS_BY_INTERFACE.md.

## Slide 15
TARGET STANDARDS STACK
TFS ↔ ns-3: what exists today, what is coming
AVAILABLE NOW
EMERGING · 2026–28
Job control
start, steer, stop what-if runs
★ 3GPP TS 28.561 NDTJob over TS 28.532 REST
3GPP Rel-20 NDT phase 2 (TR 28.883)
ITU-T Y.3092 NDT-m interface
ITU-T Q.SDTN twin signalling protocol
State sync
live topology, RF state, KPIs
★ TFS NBI + KPI/telemetry components
Rel-20 NDT data collection
YANG-Push (RFC 8641) · gNMI · Y.3092 NDT-p
IRTF NMRG twin interface drafts
Shared models
what the graph and data mean
★ IETF RFC 8345 topology (TFS ietf_network NBI)
Multi-twin collaboration (TR 28.883)
ITU-T Y.3093 data · Y.3094 model domain
O-RAN nGRG digital-twin research
Frameworks: ITU-T Y.3090 · ETSI GR ZSM 015 · IRTF NMRG twin architecture ★ = our recommended stack
Notes: Where the TFS to ns-3 link should go. Job control: 3GPP TS 28.561 models each what-if as an NDTJob managed through TS 28.532 REST operations (ITU-T Y.3092 NDT-m). State sync: TFS already ships KPI manager, telemetry and Kafka components that are not yet deployed; YANG-Push (RFC 8641) or gNMI would feed them from the radios (Y.3092 NDT-p). Shared models: TFS's ietf_network NBI plugin exposes RFC 8345 topology, which the ns-3 generator could read instead of TFS's own JSON. Emerging: 3GPP Release 20 NDT phase 2 (study TR 28.883), ITU-T Q.SDTN (SG11, under study, target around December 2026), Y.3093/Y.3094, IRTF NMRG drafts, O-RAN nGRG digital-twin research.

## Slide 16
GAP REGISTER
Top ten gaps, ranked by risk
RISK
GAP
WHERE
HIGH
1. Fallback constants labelled as ns-3 results
tsn_simulation_runner.py
HIGH
2. Failed TFS write reported as success
digital_twin_routes.py · web_dashboard.py
HIGH
3. Intent keys don't match driver keys
adapter.py ↔ CeragonDriver.py
HIGH
4. Device state is canned, not read back
ceragon/client.py
HIGH
5. admin/admin, verify=False, creds in wire log
descriptors · clients
MED
6. No telemetry subscription from radios
CeragonDriver.SubscribeState
MED
7. Drift detected on synthetic data, never fixed
assurance/reconciler.py
MED
8. Retune passes GHz as frequency_mhz
tfs_digital_twin_api.py
MED
9. Core cer_intent package has no tests
cer_intent/
LOW
10. Duplicated modules, Windows paths, fixed host
root · src/ · tfs_unity/
Notes: 1. tsn_simulation_runner.py returns constants when SSH fails and labels them 'ns-3.45-discrete-event (Simulation Engine)'. 2. The run-loop POSTs to /tfs-api/device/{uuid}/config (not a TFS endpoint) and sets applied_to_tfs = True on exception (cer_intent/api/digital_twin_routes.py, web_dashboard.py). The TFS status check counts HTTP 404/500 as ONLINE. 3. CER-Intent sends /interface[name=...]/modulation {min,max}; the driver reads mrmc_script_id, tx_frequency, tx_power_dbm and /device/operating_parameters frequency_mhz, tx_power_dbm. 4. ceragon/client.py get_device_state() returns hard-coded MH-T261 values. 5. Descriptors and defaults use admin/admin over HTTP; requests use verify=False; the restconf-wire endpoint echoes credentials; CORS * and Flask debug on by default. 6. SubscribeState/UnsubscribeState return True. 7. telemetry_simulator.py is sinusoidal; reconciler never re-applies. 8. validate_and_close_loop passes target_ghz (64.8) as frequency_mhz and 2000 as channel_id. 9. No tests for cer_intent/ (only ceragon_tfs_adapter and the driver patch have tests). 10. Root and src/ copies (tsn_simulation_runner diverged), tfs_unity/ vendored copy, c:\CER_Intent paths in several modules, ns-3 host hard-coded to efid@cersrv-029.

## Slide 17
ROADMAP
Three phases from demo to working twin
1 Make it truthful
weeks
Label mock and fallback output
Propagate TFS and driver errors
One key contract: intent ↔ driver
Live device read-back
Secrets out of repos; TLS on
Tests for cer_intent
Exit: every number on screen is real or labelled
2 Make the loop real
1–2 quarters
What-if as TS 28.561 NDTJob API
Gates computed from ns-3 KPIs
Telemetry: YANG-Push → TFS KPI/Kafka
Post-commit verify + rollback
Pluggable parsers: Gemini · Qwen · Claude
Measure real loop time
Exit: one storm scenario closes the loop on hardware
3 Standards & AI/ML
2026–27
Expanded transport skill bank
RFC 8345 topology into ns-3
Y.3092 NDT-m / NDT-p split
ns3-ai Gym env for RL agents
TS 28.105 + Y.3181 model gating
Track Rel-20 NDT, Q.SDTN
Exit: ML policies validated in the twin before deploy
Notes: Phase 1 closes the high-risk gaps in the gap register so the demo shows only real or labelled data. Phase 2 turns the what-if into a real job: expose ns-3 runs through a TS 28.561-style NDTJob API, compute the pre-flight gates from the simulated KPIs, stream radio telemetry into TFS's KPI/telemetry/Kafka components, verify after commit and roll back on regression. Add pluggable intent parsers next to Gemini: an on-prem Qwen model for air-gapped sites and Claude via the Anthropic API, selected by configuration with the regex parser as the last fallback. Then measure the true end-to-end loop time. Phase 3: expand the architect's skill bank well beyond today's nine skills to cover transport knowledge (ACM and MRMC planning, rain and multipath fade margins, XPIC and space diversity, 1+1 HSB and ring protection, LAG and multi-band aggregation, QoS and slicing, synchronisation, energy saving, capacity planning). Feed the ns-3 generator from RFC 8345 topology, split twin interfaces per Y.3092, and wrap scenarios as ns3-ai Gymnasium environments so RL agents (for example the MARL-RIC MAPPO policy) train and are gated per TS 28.105 and Y.3181 before deployment.

## Slide 18
SUMMARY
A real foundation, an honest gap list
52 · 1,143
intents parsed · configs applied
22 / 22
twin tests passing
3 steps
real RESTCONF stage → commit → discard
Next 4 weeks
Phase 1: label mocks, fix error handling and key contract, live read-back, secrets.
Then
Phase 2: NDTJob what-if, KPI-based gates, telemetry, verify and rollback.
Ask
Lab time on cersrv-029 and the MH-T261 to measure the real loop.
Notes: Real today: the intent pipeline with Gemini and rule parsing, the TFS NBI integration, the ns-3.45 TSN scenario over SSH, the TFS to ns-3 generator and the Ceragon RESTCONF stage/commit/discard driver. The gap register lists what is mocked. The roadmap turns the demo into a working closed loop.