## Slide 1
⚡ TELECOM DIGITAL TWIN ARCHITECTURE
Digital Twin Adapters & Standards
How Intent, ETSI TeraFlowSDN, NS-3 Co-Simulation, and Ceragon Microwave Hardware Interconnect
• What are the Adapters? Software translators bridging heterogeneous timing, data formats, and control protocols.
• International Standards: Anchored in TM Forum TMF921, 3GPP TS 28.561, ITU-T Y.3090, IETF DTI, and RFC 8040 RESTCONF.
• Closed-Loop Automation: Zero-risk What-If discrete prediction prior to physical hardware 2-phase commit actuation.
Ceragon Networks & ETSI TeraFlowSDN Research • Standalone & Production Hybrid Architecture

## Slide 2
THE PROBLEM & ARCHITECTURAL NEED
The Core Problem: Why Do We Need Adapters?
💡 In a Telecom Digital Twin, components speak completely different languages and operate at vastly different timescales. Adapters are the critical translators that bridge this semantic and temporal chasm.
1. Declarative Intent
Human Operator / SLA
Speaks: Natural Language / JSON
Timescale: Minutes to Days
Key Data: "Ensure URLLC latency < 1.5ms and 99.999% availability during storms"
2. SDN Controller
ETSI TeraFlowSDN
Speaks: Context DB, gRPC, CSPF
Timescale: Seconds (Control Plane)
Key Data: Device UUIDs, Endpoints, Topology Graphs, TI-LFA backup paths
3. Discrete Simulator
NS-3 Discrete Core
Speaks: C++ Event Queue & Packets
Timescale: Microseconds (t = 0.000s)
Key Data: QueueDisc buffer drops, WiFi EDCA AC_VO, link propagation delay
4. Physical Hardware
Ceragon MH-T261
Speaks: RFC 8040 RESTCONF & PHY
Timescale: Sub-millisecond Hardware
Key Data: V-Band 60.48 GHz, ACM MCS 0-9, PHY RSSI/SNR, RF registers

## Slide 3
INTERNATIONAL STANDARDS REFERENCE
Standards for Digital Twin APIs We Use & What They Are
3GPP TS 28.561 [PRIMARY APPROVED ANCHOR]
NDT Management Service & NdtJob Model
Standard: Approved 3GPP Rel-18/19 specification standardizing the NDT_MnS, NdtJob model, and simulation result semantics.
In Our Platform: Primary Anchor for TeraFlow-to-NS-3: TFS instantiates an NdtSimulationJob, runs scoped co-simulation, and ingests standardized SimulationResult (PDB, PER, breach prediction).
ITU-T Q.5040 [FUTURE SIGNALING PROTOCOL]
Signaling Architecture & Control for DTN
Standard: ITU-T SG11 standard defining signaling procedures for simulation task invocation (Sim-Task-Req), execution control, and KPI streaming.
In Our Platform: The likely future signaling standard over the wire for our REST/JSON and SSH RPC bridge between TeraFlowSDN and NS-3 on cersrv-029.
ITU-T Y.3090 / Y.3092 [DTN ARCH & MMEF]
DTN Architecture & Model Management (MMEF)
Standard: ITU-T SG13 3-layer DTN model (Y.3090) and Model Management & Execution Framework (Y.3092) for model fidelity selection.
In Our Platform: Dictates our 5-Tier Simulation Resolution Governor (balancing model accuracy vs computation time) and shadow datastore sync.
TM Forum TMF921 [BUSINESS & SLA]
Intent Management REST API
Standard: REST API standard for expressing declarative network intent and SLA expectations.
In Our Platform: Operator defines latency (< 1.5ms) and availability without writing low-level scripts. Tracks intent state: Acknowledged → In Evaluation → Compliant.
IETF RFC 8040 / 7950 [HARDWARE SBI]
RESTCONF Protocol & YANG 1.1
Standard: IETF standard for HTTP-based network device management accessing YANG data stores.
In Our Platform: Southbound interface to Ceragon MH-T261 (192.168.1.225:80). Provides Candidate Datastore staging, diff validation, and 2-Phase Commit (2PC).
ETSI TeraFlowSDN APIs [SDN CONTROL]
Cloud-Native SDN Controller Microservices
Standard: ETSI standard cloud-native gRPC microservices pipeline for autonomous transport networks.
In Our Platform: Exposes Context Service (gRPC :10010), Service/PCE (gRPC :10030), Device Driver (gRPC :10020), and Monitoring Telemetry Daemon (gRPC :10040).

## Slide 4
HOW THE ADAPTER FUNCTIONS
Adapter 1: TeraFlow-to-NS-3 Simulation Adapter (3GPP TS 28.561 & Q.5040)
🔁 Step-by-Step Functional Flow (3GPP TS 28.561 & Q.5040)
Step 1: TFS Context → 3GPP NDTI State Sync The adapter queries ETSI TeraFlowSDN (:8088 Context) to populate the active 3GPP Network Digital Twin Instance (NDTI) with live 34-node topology, link capacities, and Ceragon RF metrics (RSSI -58 dBm, MCS 8).
Step 2: 3GPP NdtJob Creation & Y.3092 Scoping Instantiates a standardized 3GPP NdtSimulationJob. The ITU-T Y.3092 Governor automatically scopes the graph to Tier 4: URLLC Micro-Packet (23 nodes, 95% fidelity) executing in ~1150ms.
Step 3: Q.5040 Simulation Task Signaling Dispatches task to discrete core on cersrv-029 following the ITU-T Q.5040 signaling pattern (Sim-Task-Req), injecting a 3.5x bulk traffic surge (bufferbloat) or ITU-R P.838 rain fade.
Step 4: 3GPP SimulationResult Semantics & Trace Ingestion Ingests standardized 3GPP SimulationResult semantics (predicted PDB latency, PER loss, queue depth, slaBreachPredicted verdict) and discrete NetAnim trace to gate physical actuation.
⚙️ Key Implementation Features
• 3GPP TS 28.561 NDT_MnS: Implements approved 3GPP NDT management service operations: job parameterization, target subnetwork scoping, and simulation result semantics.
• ITU-T Q.5040 Signaling: Adopts the emerging Q.5040 task invocation and report signaling pattern between ETSI TeraFlowSDN and the remote NS-3 simulation engine.
• Multi-Tier Y.3092 Governor: 5 Resolution Tiers (Macro-Topology 25%, Queue Dynamics 55%, Physical RF 75%, URLLC 95%, Green Energy 20%).
• NetAnim Discrete Replay: Instruments AnimationInterface for real timeline playback (0.000s - 2.500s) with 10 visual buffer slots and tail-drop alerts.
• Remote Execution Core: Dispatches via SSH/JSON to ns-3.45 on efid@cersrv-029; falls back to analytical local simulation for zero-dependency standalone mode.
• Multi-Tier Governor: 5 Resolution Tiers (Macro-Topology 25%, Queue Dynamics 55%, Physical RF 75%, URLLC 95%, Green Energy 20%).
• NetAnim XML Output: Instruments AnimationInterface for real timeline playback (0.000s - 2.500s) with 10 visual buffer slots and tail-drop alerts.
• Deterministic TSN Mapping: Maps 802.1Q PCP Class 6 & EDCA AC_VO into PfifoFast Band 0 priority queues.

## Slide 5
PHYSICAL ACTUATION & TELEMETRY
Adapter 2: TFS Southbound & Hardware Driver Adapter
📝 STAGE 1
Candidate Datastore Staging
Translates AI Decision Engine output into concrete YANG configuration rules staged in ETSI TeraFlowSDN's Candidate Datastore (RFC 8040).
• Target Device: Ceragon MH-T261 (UUID f676623c...)
• ACM Floor Hardened: MCS 0 → MCS 4 (≥ 500 Mbps min)
• QoS Queue: FIFO → IEEE 802.1Q PCP Class 6 (PfifoFast)
• Carrier Frequency: 60.48 GHz → 64.80 GHz
🛡️ STAGE 2
Pre-Flight Safety Envelope Gate
Before touching physical production traffic, 3GPP TS 28.561 requires verification of the candidate configuration against live constraints.
• Gate 1: Latency Bound Pass (Predicted 1.12ms ≤ 1.5ms)
• Gate 2: Queue Stability Pass (Buffer occupancy < 40%)
• Gate 3: Hardware Capability Pass (MH-T261 supports MCS 4)
• Gate 4: Spectral Mask Pass (64.80 GHz approved in V-Band)
🚀 STAGE 3
RFC 8040 RESTCONF 2PC Commit
Executes Two-Phase Commit transaction directly over HTTP/RESTCONF to physical transceiver socket 192.168.1.225:80.
• Phase 1 (Prepare): PATCH candidate datastore via RESTCONF
• Phase 2 (Commit): POST ietf-netconf:commit operation
• Telemetry Verification: Continuous RFC 8040 poll
• Instant Rollback: Automatic 2PC revert if health checks fail
🔒 Zero-Outage Guarantee: By combining Candidate Datastore staging, Pre-Flight discrete validation, and 2-Phase Commit, the adapter ensures that bad configurations are rejected in software before they can impact customer SLA.

## Slide 6
ARCHITECTURE SUMMARY
Summary: End-to-End Closed-Loop Operational Value
🛡️ Zero-Risk What-If Validation
Predictive Discrete Simulation
Operators can test severe perturbations (3.5x bulk surges, category-5 tropical rain fade, fiber link cuts) in a microsecond-accurate digital twin without putting live production circuits at risk.
🌐 Standardized Multi-Vendor Interoperability
Anchored in 3GPP, ITU-T & IETF
Zero proprietary lock-in. Built entirely on open telecom specifications: TM Forum TMF921 Intent API, 3GPP TS 28.561 NDT lifecycle, ITU-T Y.3090, IETF DTI, and RFC 8040 RESTCONF.
⚡ Sub-Second Autonomous Closed Loop
Autonomous Self-Healing Transport
Replaces hours of manual CLI troubleshooting with autonomous, closed-loop assurance: SLA intent is ingested, simulated in NS-3, safety-verified, and actuated via TFS in ~1.9 to 2.2 seconds total.
📋 Digital Twin Adapter Quick Reference Table
• Intent Adapter: Translates Natural Language / SLA bounds into TFS Service & CSPF requests (TM Forum TMF921).
• Simulation Adapter: Syncs TFS live graph into NS-3 C++ discrete engine, scopes fidelity (Tiers 1-5), and outputs microsecond traces.
• Southbound Driver: Manages candidate datastore diffs and 2-phase commits to Ceragon MH-T261 via RFC 8040 RESTCONF.